Header of buffer entry
Ethernet package
0x2001
0x0040
Bytes 4 - 9
MAC destination address
Bytes 64 - 67
CRC sum
Bytes 16 - 63
Ethernet payload
Bytes 2 and 3
Packet length in bytes
In this case, 0x40 = 64
Bytes 10 - 15
MAC source address
Bytes 0 and 1 – packet status
Bit 15: multicast package
Bit 14: packet matching address
Bit 13: broadcast package
Bit 0: frame ok
So in this case, this is a valid broadcast
package

---
Bytes 72 - 135
Bytes 0 - 1
Bytes 2 - 3
Bytes 4 - 67
Bytes 68 - 69
Bytes 70 - 71
Bytes 208 - 271
Bytes 204 - 205
Bytes 206 - 207
Bytes136 - 137
Bytes 138 - 139
Bytes 140 - 203
Bytes344 - 407
Bytes 340 - 341
Bytes 342 - 343
Bytes272 - 273
Bytes 274 - 275
Bytes276 - 339

---
Bytes 0 - 35
Bytes 8160 - 8191
First part of package
Stored at bytes 8160 - 8192
Data from previously received packages
Second part of package
Stored at bytes0 - 35
Receive 64 byte
After receiving package:
CBR = 36
CAPR = 8144
Before receiving package:
CBR = 8160
CAPR = 8144

---
MAC Layer
MMI
PHY Layer
MDI
Medium