UDP
TCP
ICMP
ip_tx_msg
ip_get_src_addr
IP
ARP
arp_resolve
Work queue IP_TX_QUEUE_ID
arp_rx_msg
ip_rx_msg
tx_msg
tx_msg
Network interface layer
Work queue NET_IF_QUEUE_ID
Device driver layer
Device N
Device 2
Device 1
. . .

---
Message buffer
Pointer in net_msg_t
data
start
ip_hdr
tcp_hdr
end
Headroom
IP
header
TCP
header
TCP
data
Available
bytes
net_msg->data + net_msg->length

---
Upper layers (IP, ARP, ...)
net_if_tx_msg
<proto>_rx_msg
Network interface layer
Work queue NET_IF_QUEUE_ID
net_if_add_nic
net_if_multiplex_msg
net_if_tx_event
tx_msg
Device driver
Device driver
Network
card
Network
card
Network
card
Network
card

---
Receive queue
We probably need different types of queues. For a stream oriented socket, this is a stream of bytes, for a datagram or raw socket, it is a queue of net_msg, as we need to
Preserve message boundaries
Socket
State
pending error
Socket
Transmit queue
Need this because receiver might not be ready to accept more data (window!)
Open File
Connection
indication
queue

---
CLOSED
listen system call
Connect system call
SYN segment sent
LISTEN
SYN received
SYN-ACK sent
SYN-RCVD
SYN-SENT
ACK received
SYN-ACK received
ACK sent
ESTABLISHED

---
The send sequence space
Stream of data
SND_UNA + SND_WND
Right hand side of send window
SND_NXT
Next sequence number to be sent
SND_UNA
SND_UNA
Smallest sequence number not yet acknowledged
Sent and acknowledged
Sent but not yet acknowledged
Waiting to be sent
Waiting for receivers buffer to empty

---
The send sequence space
U – usable window
Send window (10 bytes)
98
110
111
112
113
102
103
104
105
106
107
108
109
99
100
101
SND_UNA + SND_WND
First byte outside of window
SND_NXT
Next sequence number to be sent
SND_UNA
SND_UNA
Smallest sequence number not yet acknowledged
Sent and acknowledged
Sent but not yet acknowledged
Ready to be sent
Waiting for receivers buffer to empty

---
The receive sequence space
Receive window (10 bytes)
98
110
111
112
113
102
103
104
105
106
107
108
109
99
100
101
RCV_NXT
Next sequence number expected
RCV_NXT + RCV_WND
First byte outside of window
Received and acknowledged
Acceptable bytes
Waiting for receivers buffer to empty

---
Generic socket layer (net.c)
tcp.c
Protocol specific socket layer
(tcp_create_socket, tcp_send, tcp_rcv, tcp_bind, tcp_connect, tcp_listen, tcp_select, tcp_release)
Utilities
TCP
input
processing
(tcp_rx_msg)
TCP send
processing
(trigger_send)
TCP
timer
processing
(tcp_do_tick)
IP layer (ip.c)